## Slide 1: Image Processing on the Driver Station using Python
Dustin Spicuzza (Team 2423/1418)
December 7, 2013
Team 1418 Workshops

## Slide 2: Agenda
Why Driver Station + OpenCV + Python?
Simple demos
  hello_world.py
  hello_webcam.py
Practical Example: 2013 FRC Game
Driver Station software demo
pynetworktables

## Slide 3: Why the Driver Station
You can use any laptop for the driver station
  As much power as your team can afford
  Even really cheap laptops are more powerful than the cRio
Easier to develop/debug code on the driver station
  You can run the code on your development computer, no robot required

## Slide 4: Why OpenCV?
Originally developed by Intel
It has thousands of image processing related algorithms and functions available
  Highly optimized and reliable
  Has building blocks that fit together
Lets you do complex image processing without needing to understand the math
  If you understand the math, it helps!

## Slide 5: Why OpenCV?
Bindings for multiple languages
  C/C++
  Java
  Python
Multiple platforms supported
  Windows
  Linux
  OSX
  Android
Oh, and it’s FREE!

## Slide 6: What OpenCV provides
Image I/O:
  Read/Write images from disk
  Use native OS functionality to interface with cameras
Image Segmentation
  Edge finding
  Contour detection
  Thresholding

## Slide 7: What OpenCV provides
Face detection
Motion tracking
Stereo vision support
Support for GPU acceleration
Machine learning operations
  Classifiers
  Neural networks

## Slide 8: What OpenCV provides
Distributed with lots of useful samples that you can use to figure out how OpenCV works
  Face detection
  Edge finding
  Histograms
  Square finder
  Lots and lots and lots of stuff…

## Slide 9: Why Python+OpenCV?
Python is really easy to learn and use
  Simple syntax
  Rapid prototyping
Most of the compute intensive work is implemented in C/C++
  Python is just glue, realtime operation is possible
NumPy is awesome
  Manipulating image data is trivial compared to other OpenCV bindings (Java, C++)

## Slide 10: Hello World!
Create an image, show it using the GUI
import cv2
import numpy as np
# create a numpy array to hold the data
# -> w=200, h=100, channels=3
img = np.zeros(shape=(100,200,3), dtype=np.uint8)
# write red text to image (note BGR, not RGB!)
cv2.putText(img, "Hello World!", (50,50),
cv2.FONT_HERSHEY_PLAIN, 1, (0,0,255))
cv2.imshow('Image', img)
cv2.waitKey(0)

## Slide 11: Hello Webcam!
Capture from a webcam, show it
import cv2
vc = cv2.VideoCapture()
if not vc.open(0):
print "Could not connect to webcam"
exit(1)
while cv2.waitKey(30) <= 0:
success, img = vc.read()
if not success:
break
cv2.imshow("Webcam", img)

## Slide 12: OpenCV Image Basics
Images are stored as multidimensional arrays
  Color images have 3 dimensions: height, width, channel
Each pixel is a number stored in the array
Numpy array notation allows you to do operations on individual pixels or ranges of pixels
img[24, 42, 0] # access a single pixel
img[24:42, 42:100, :] # access a range of pixels

## Slide 13: OpenCV Image Basics
Color is represented by storing combinations of Red, Blue, and Green pixels in separate channels
  OpenCV uses BGR representation, not RGB
The amount of each individual color is represented in the individual channel
  ‘dark’ is zero, ‘bright’ is 255
Combine the channels to represent a color
  Green = RGB( 0, 255, 0 )
  Deep Pink = RGB( 255, 20, 147 )

## Slide 14: Practical Example
2013 challenge: find targets that are surrounded by retroreflective tape, and shoot frisbees into them
  The tape reflects light directly back at source
Src: http://frc-manual.usfirst.org

## Slide 15: Practical Example
Finding gray tape at a distance isn’t particularly easy
  Key part of image processing is removing as much non-essential information from image
We can do better!
  Shine bright LEDs at the target and the tape reflects that color back to the camera
    Many teams have found that green light works best
  Reduce exposure of camera so only bright light sources are seen

## Slide 16: Practical Example
Result:

## Slide 17: Practical Example
Processing steps to find targets
  Isolate the green portions of the image
  Analyze the green portions to determine targets

## Slide 18: Identify the green
What is “green” anyways?
    This is green. This is also green.
To a computer, green is really a range of colors
  An object’s color changes depending on lighting conditions
We can transform the image to identify colors independent of lighting conditions

## Slide 19: Identify the green
Convert the image from RGB to HSV
  Hue: the color
  Saturation: Colorfulness
  Value: Brightness
http://en.wikipedia.org/wiki/File:Hsl-hsv_models.svg
hsv = cv2.cvtColor(img,cv2.cv.CV_BGR2HSV)

## Slide 20: Identify the green
Split view of converted image (H, S, V)
Compression artifacts are clearly present
H
S
V

## Slide 21: Identify the green
Green is a range of values present in the image
‘Threshold’ the image to get rid of the colors that we don’t care about
Lots of ways to do this
  Manually specify values
  Automated methods

## Slide 22: Identify the green
We can use the ‘Threshold’ function to find values between a low and high value
  Wanted values are converted to 255
  Unwanted values are now 0
def threshold_range(im, lo, hi):
unused, t1 = cv2.threshold(im, lo, 255, type=cv2.THRESH_BINARY)
unused, t2 = cv2.threshold(im, hi, 255, type=cv2.THRESH_BINARY_INV)
return cv2.bitwise_and(t1, t2)

## Slide 23: Identify the green
Threshold each channel, combine the results
Note there are little holes in the image where the color doesn’t quite line up…

## Slide 24: Identify the green
We can use a morphological operation to fill in the holes
  Various types of morphology operations available
They modify a pixel based on the values of its neighboring pixels
  The one we use to fill in holes is a “closing” operation
kernel = cv2.getStructuringElement(cv2.MORPH_RECT, (2,2), anchor=(1,1))
output = cv2.morphologyEx(img, cv2.MORPH_CLOSE, kernel,
iterations=9)

## Slide 25: Identify the green
  The output looks a lot better now!

## Slide 26: Identifying Targets
Use findContours() to find regions of interest
  Returns a list of points bounding each separate blob in the image (called a contour)
  There’s a drawContours function
  Also returns a hierarchy so you can determine whether a contour is entirely inside another contour

## Slide 27: Identifying Targets
Contour analysis
  Discard non-convex contours
  Convert to polygon approximation (approxPolyDP)
  Discard polygons that aren’t rectangles
  Find a minimal rotated bounding rectangle to perform analysis on (minAreaRect)

## Slide 28: Identifying Targets
Target analysis
  Determine ratio of rectangle sides to see if they match target sizes
  Ensure rectangles have at least one horizontal line and two nearly vertical lines
  Remove duplicates (inner part of rectangle)

## Slide 29: Identifying Targets
Target analysis
  Determine from ratio (w/h) whether it’s a top/middle/low target
    Targets at each level are different sizes
  Determine from relative position whether it’s the left or right target we’re looking at
    The left middle target will always be the target left of a top target, etc..

## Slide 30: Identifying Targets
Draw pretty pictures and labels, and we’re done!

## Slide 31: Getting the data to the robot
We identified the targets… now what?
You can use NetworkTables to get the data there
  On the robot, it’s in WPILib (C++, Java, LabVIEW)
  Off the robot, SmartDashboard talks to the robot via NetworkTables
  In python, we use pynetworktables to communicate via NetworkTables

## Slide 32: Getting the data to the robot
Sample code to transmit a number via NetworkTables in python:
from pynetworktables import NetworkTable
# Set the robot’s IP address here
NetworkTable.SetIPAddress(‘10.24.23.2’)
NetworkTable.SetClientMode()
NetworkTable.Initialize()
table = NetworkTable.GetTable('SmartDashboard')
table.PutNumber(‘name’, 1)

## Slide 33: Want fully-functioning code for this?
Team 2423 implemented all of this in their driver station in 2013
  We even won an award!
  You can download the code at http://www.virtualroadside.com/FRC/

## Slide 34: Resources
Python 2.7.x
  http://www.python.org/download/releases/2.7.6/
Learn python
  http://www.codecademy.com/tracks/python
OpenCV 2.4.x
  http://opencv.org/
Numpy 1.7.x
  Official site: http://www.numpy.org/
  Optimized builds: http://www.lfd.uci.edu/~gohlke/pythonlibs/#numpy

## Slide 35: Resources
pynetworktables
  source code + examples https://github.com/robotpy/pynetworktables
  windows downloads http://firstforge.wpi.edu/sf/projects/robotpy
Edit & debug python code using Eclipse
  Pydev: http://pydev.org/

## Slide 36: Questions?

## Slide 37: Thanks to
FRC Team 341, whose image processing code was the base for our code in 2013
Sam Rosenblum and Stephen Rawls